## Slide 1
Remote Station Operation Using Wfview
Ed James KA8JMW
John Maxwell W0VG

## Slide 2: Todays Presentation on Wfview
This quick explanation of the Wfview implementations and not intended to be a comprehensive how-to.
There are quite a few how-to videos out.
Significant functionality is being “glossed over” in this quick talk.

## Slide 3: What is
A free, open source, program that allows many modern Icom and Kenwood ham radio transceivers to be controlled via a computer.
Displays the spectrum display on whatever display is connected, including projectors, touch screens, and TVs.
Allows for full radio control from a computer keyboard and basic control from a numeric keypad.
Runs on hardware ranging from the Raspberry Pi to laptops to desktops.
Runs on Linux, macOS, and Windows.
Supports rig control over ethernet as well as over USB & serial CIV bus.
Allows older radios to be accessed over the internet, for full control and low-latency audio streaming

## Slide 4: Typical Wfview Configurations
KA8JMW 1-31-2024
Radio with USB or Serial Interface
Radio with an Ethernet Interface

## Slide 5
Supports many USB Controllers
RC-28, Shuttle, Stream Deck, sunSDR, …

## Slide 6: Stream Deck+ and Wfview
• Can be used for all radio functions in Wfview
  • VFOA/VFOB
  • Waterfall/Spectrum
  • Volume
  • RF Gain
  • TX Power
  And more
• Multiple “pages” of options can be addressed
• Commonly used function on front page
• Less common on second page

## Slide 7: Stream Deck+ Device Configuration
You do not need to load any drivers
Wfview software polls and operates the device directly
Simply Right Click on the button and select its function

## Slide 9: Demonstration
Using a Remote IC-7760 Located in RMHAM trailer

## Slide 10
WFVIEW CLIENT
(LOCAL)
WFVIEW SERVER
(REMOTE)
STREAM DECK PLUS
IC-7300
Digital Modes
When operating digital modes you will need a Virtual Audio Cable to provide the audio to both Wfview & the digital mode program.
Excessive latency can be an issue.

## Slide 11
VB-Audio Virtual Apps
FREE for both Windows & Mac

## Slide 12
(Questions?)

## Slide 13: Thank You
Ed James KA8JMW, ka8jmw@arrl.net
John Maxwell, W0VG johnm@johnmaxwell.net
http://www.rmham.org